## Slide 1: Aim
This project intends to find a novel way of powering a device without the use of battery power
  Investigate an extreme environment
  Find a suitable way to power a device and design a solution
  The goal upon completion is to have a well thought out design that could be built and used in the real world

## Slide 2: Extreme Environment: The Sea
The sea cover approximately ¾ of the earths surface
Relatively unexplored due to harsh environment: Temperatures, pressures, no oxygen
A robot could be used
If no batteries then it could stay underwater for indefinite periods!

## Slide 3: Specification
A robot that is able to move under its own power while:
  Withstanding temperatures: 3 - 21 ̊C
  Withstanding pressures: 1 atmosphere for every 10m underwater
  Withstanding corrosion from salt water
  No turning functionality
  No control ie. goes forward when has power, idle otherwise
  These things to be added after initial design proven

## Slide 4: Undersea Challenges
To stop water from getting in, it must be water tight but to stop the pressure from crushing it, the robot must be filled with a non-compressible, non-conducting liquid, a good choice is therefore oil.
To avoid rust the exterior of the robot will be made from plastic
Tank tracks will be used to give maximum traction and to spread weight to stop sinking occurring in the soft sediment

## Slide 5: Theory of Operation

## Slide 6: Turbine
Size of turbine determines the power available:
Robot will require 25W of power including power loss to power converter inefficiency
  Diameter of turbine is 23.8 cm

## Slide 7: Testing – Generator
Chart: Voltage (V)
| 0 | 0.31100000000000011 | 0.52 | 0.75200000000000022 | 0.99099999999999999 | 1.256 | 1.486 | 1.7260000000000004 | 1.97 | 2.2090000000000001 | 2.4619999999999997 | 2.698 | 2.9289999999999998 | 3.1669999999999998 | 3.4079999999999999 | 3.6359999999999997 | 3.855999999999999 | 4.1049999999999986 | 4.3339999999999996 | 4.54 | 4.7639999999999985
5Ω | 0 | 0.019344 | 0.05408 | 0.1131 | 0.19642 | 0.31551 | 0.44164 | 0.59582 | 0.77618 | 0.97594 | 1.2123 | 1.4558 | 1.7158 | 2.006 | 2.3229 | 2.6441 | 2.9737 | 3.3702 | 3.7567 | 4.1223 | 4.5391
1Ω | 0 | 0.085849 | 0.251 | 0.53876 | 0.92737 | 1.44 | 2.0707 | 2.7556 | 3.6214 | 4.5753 | 5.6406 | 6.8069 | 8.1225 | 9.61 | 11.1489 | 12.6736 | 14.5695 | 16.3539 | 18.5502 | 20.6298 | 22.6862
0.5Ω | 0 | 0.08 | 0.35786 | 0.83205 | 1.5103 | 2.4112 | 3.5538 | 4.8112 | 6.2729 | 8.016 | 9.9102 | 11.9854 | 14.4507 | 16.9595 | 19.7192 | 22.5792 | 25.6328 | 29.0017 | 32.2886 | 35.9552 | 39.3917
E
R = 0.034 Ω
L = 0.000478 H

## Slide 8: Generator Test Results
Maximum Power Output at 0.5Ω = 70W
Speed required for 25W = 2400rpm
Voltage given at 2400rpm = 4.7 V
Current given at 2400 rpm = 5.4 A
Gearbox required is 19:1
Power converter must convert from 4.7V, 5.4A AC to 5V, 2A DC
Parallel output motors to decrease resistance to approximately 0.36Ω

## Slide 9: Conclusions
A method of powering a remote device underwater has been achieved with a preliminary design made
Future Steps
  Build tank tracks and use with motors to find exact characteristics
  Choose and purchase power converter
  Build and Test
Nathan Rich
Supervisor: Pat Bodger
Acknowledgments: Alan Wood, Bill Heffernan